ID	Group	Name	Return	Parameter	Annotations/Description
0	Tasking	execute	FS_ERROR	Path, argc, argv[]	Executes the executable at path
1		createThread	uint32_t	void (*)(), priority (int)	Executes the function given in a separate thread with the specified priority. Returns the ID of the new task
2		exit	void		Exits from the current thread/task
3		wait	bool	Reason, data, timeout	Locks a task until the timeout is reached (return false) or the reason for the block has gone
4		createConsoleThread	uint32_t	void (*)(), priority (int), name	Executes the function given in a separate thread with the specified priority in a new console. Returns the ID of the new task
5
6
7
8
9
10	Memory Management	userHeap_create	Handle	size_t	Creates a new user heap with given initial size
11		userHeap_destroy	void	Handle	Frees user heap
12		userHeap_alloc		Handle, Size	Allocates memory on the given user heap
13		userHeap_free		Handle, Address	Frees memory on the given user heap
14
15	File	fopen	file-struct*	Path, mode (const char*)	Like in C standard library
16		fgetc	char		Like in C standard library
17		fputc	error		Like in C standard library
18		fseek	error		Like in C standard library
19		fflush	error		Like in C standard library
20		fmove	error	Source, Destination, copy	If destination is 0, the file is removed, otherwise its moved from source to destination. The function allows movement between different partitions. A copy is created, if copy is true.
21		fclose	error		Like in C standard library
22		partition_format	error	Path (char*), FS_t, name (char*)	Takes the path, the desired filesystem type and name and formats the partition
23		folderAccess			Opens directory handle
24		folderClose			Closes directory handle
25	IPC	ipc_fopen	IPC_ERROR	Path, Destination, Mode (const char*)	Opens a file in the IPC tree. The file saved in destination can be used as any other file
26		ipc_getFolder	IPC_ERROR	Path, Destination, Length	Writes all subfolder names into Destination. Separation: |
27		ipc_getString	IPC_ERROR	Path, Destination, Length (size_t*)	Returns a string from the IPC-tree. The string is written into the second parameter. If Length is not sufficient, the required length is written back into it.
28		ipc_setString	IPC_ERROR	Path, Source	Fills in a string to the IPC-tree
29		ipc_getInt	IPC_ERROR	Path, Destination	Returns an Integer from the IPC-tree (64-bit)
30		ipc_setInt	IPC_ERROR	Path, Source	Fills in an Integer to the IPC-tree (64-bit)
31		ipc_getDouble	IPC_ERROR	Path, Destination	Returns a double precision floating point number from the IPC-tree
32		ipc_setDouble	IPC_ERROR	Path, Source	Fills in a double precision floating point number to the IPC-tree
33		ipc_deleteKey	IPC_ERROR	Path	Deletes a value from the IPC-tree
34		ipc_setAccess	IPC_ERROR	Path, Rights, TaskID	Allows a task/user to access that key
35		ipc_setWorkingNode	IPC_ERROR	Path, Create	Sets working node (shortcut >) to given path, creates the node if Create is true
36	Event system
37		waitForEvent	!Timeout (bool)	Timeout	Stops calling task until an event occurred or timeout reached. Timeout 0 means, no timeout.
38		event_enable		bool	Informs the OS, whether we will handle events or not. Default is false.
39		event_poll	Type (uint32_t)	Buffer (void**)	Returns the first event from the event queue and stores the data in the given buffer. If the length of the data exceeds its bounds, the function returns 1. If no event is available, it returns 0.
40	Getting information quickly	getCurrentMilliseconds	uint32_t		Returns the time elapsed since boot in milliseconds
41
42
43
44
45
46
47
48
49
50	System control	systemControl		SYSTEM_CONTROL (enum)	Advices the system to do something (Reboot, etc.)
51		systemRefresh		SYSTEM_INFO (enum)	Makes the system refreshing the specified Information
52
53
54
55	Graphics	putchar	int	char	Prints a character to the screen at the cursors position
56		textColor		uint8_t (color)	Sets the colour of the following text output
57		setScrollfield		Top, bottom	Sets the borders of the scrolling area
58		setCursor		Position	Sets the position of the write cursor
59		getCursor		Position*	Writes the position of the write cursor to the given address.
60		readChar	char	Position	Reads a char from the userscreen at the specified position
61		clearScreen		uint8_t (color)	Clears the userscreen
62		console_setProperties		console_properties_t	Sets properties of the console that belongs to the current task
63		refreshUserScreen			Updates the screen.
64
65
66
67
68
69
70	User input
71		keyPressed	bool	Key (enum)	Returns true if the specified key is pressed
72		mousePressed	bool	Mousebutton (enum)	Returns true if the specified button is pressed
73		getMousePosition		Position*	Writes the position of the mouse cursor to the field passed as argument
74		setMousePosition		x, y	Sets the position of the mouse cursor
75
76
77
78
79
80	Sound	beep		Frequency, duration	Beeps with the specified frequency for duration in milliseconds
81
82
83	Network	dns_getServer		IP_t* server
84		dns_setServer		IP_t server
85		tcp_connect	ID (uint32_t)	IP, port
86		tcp_send		ID, data, length
87		tcp_close		ID
88		udp_send
89		udp_bind
90		udp_unbind
91		getMyIP